## Slide 1: IGD-TP EF6 CORI MIND WP1
Improving the geological safety case knowledge of the behaviour of organic containing long-lived intermediate level wastes

## Slide 2: MIND WP1 Objectives
Reduce uncertainty of safety-relevant microbial processes controlling radionuclide, chemical and gas release from long-lived intermediate level wastes (ILW) containing organics (SRA Key topic 2 sub topic 2)
  To quantify the combined rates of biodegradation, radiolysis and hydrolysis of anthropogenic organic polymers and cellulose present in ILW under disposal conditions.
  To identify key chemical species resulting from organic ILW biodegradation, radiolysis and hydrolysis and their effects on radionuclide speciation and mobility.
  To establish the in situ chemical and physical conditions that may limit microbial activity in EU repository concepts for ILW utilising cementitous materials within a neutral pH host rock.
  To examine the microbial generation and consumption of CH4 and H2 under ILW repository conditions.
  To understand the effect of ILW heterogeneity on bioprocess pathways, pH and redox conditions, barrier degradation and radionuclide release.

## Slide 3: Task 1.2
Rate and mechanism of biodegradation of ILW organic polymers affected by radiation, under repository relevant conditions.
  60Co ϒ irradiation of organics
  Mostly high pH Ca(OH)2 buffered conditions
  Study biodegradation of radiolysis products by;
    cement pH adapted microbes at high pH,
    indigenous microbes from URLs under neutral pH
  Radionuclide interactions with degradation products

## Slide 4: Organic Materials
Halogenated organics (PVC) including additives (e.g. pthalates)
  Manchester; irradiation, biodegradation and radionuclide redox studies
Ion exchange resins (DVB styrene)
  Irradiation at Manchester
  Lab and in situ biodegradation studies at EPFL
  Irradiation and biodegradation by RCR-REZ and TUL
Bitumen
  SCK•CEN; irradiation and biodegradation

## Slide 5: Other Relevant Studies
Alkali cellulose degradation
  Manchester; effect of irradiation on CDPs
  ISA biodegradation under cement buffered and groundwater pH conditions
Radionuclide interactions
  HZDR will examine (UV-vis, TRLFS, IR, XAS) radionuclide complexation with aqueous biodegradation products from WP1 partners and with model substances
  UGR will examine radionuclide association with solid products (electron microscopy based techniques)
  Manchester bio-reduction of U etc utilising organic radiolysis products

## Slide 6: Outlook
A wide range of organic materials are present in ILW
  Degradation behaviour will depend on wasteform conditions (pH), heterogeneity etc
The MIND project begins the investigation of the combined effects of radiolysis/hydrolysis and biodegradation
Irradiation studies are mainly scheduled in the first 2 years of the MIND project
  The initial results from MIND irradiation studies should inform any future project that may result from CORI
  In later years, specific biodegradation studies could be undertaken considering radiolysis products resulting from a wider range of irradiation studies under taken by a CORI project
  Funding of future collaborations would need to be considered